## Slide 1
23CSE304 — EMBEDDED SYSTEMS
SMART AMBULANCE TRAFFIC PRIORITY AND JUNCTION MANAGEMENT SYSTEM
An Intelligent, Interrupt-Driven Controller with Anti-Starvation Scheduling on STM32C031C6
TEAM MEMBERS:
• GRS Akshitha (AM.SC.U4CSE24221)
• Sai Mohith Konduru (AM.SC.U4CSE24230)
• Nandini Kuchi (AM.SC.U4CSE24231)
• Leela Nayan P Kanjirapully (AM.SC.U4CSE24232)
• Mannsi Pentela (AM.SC.U4CSE24247)

## Slide 2
23CSE304 | EMBEDDED SYSTEMS 2 / 13
01 • BACKGROUND
Problem statement — Why ambulances need signal priority at junctions
THE CHALLENGE CRITICAL TIME LOST
• 4-Way Intersection: Congested urban junctions spanning North, East, South, and West.
• The Golden Hour: In acute cardiac and trauma cases, every 60 seconds of transit delay reduces patient survival probability by up to 10%.
• Rigid Fixed Timers: Traditional traffic controllers follow fixed timers without any perception of approaching emergency vehicles.
• Dangerous Evasion: Drivers often execute hazardous maneuvers into oncoming lanes to clear a path for trapped ambulances.
THE SOLUTION THE ISSUE & PROJECT AIM
• Collision Risk: Abruptly overriding signals creates severe broadside collision risks. Priority MUST be granted with controlled caution buffers.
• Civilian Starvation: Continuous emergency overrides along busy corridors can hold non-emergency lanes at permanent red lights.
• Project Objective: Automatically grant safe traffic-signal priority to approaching emergency vehicles via hardware interrupts.
• Core Requirement: Detect the ambulance, safely transition conflicting signals through yellow and all-red, sound warning alerts, and restore regular traffic fairly.

## Slide 3
23CSE304 | EMBEDDED SYSTEMS 3 / 13
02 • PROJECT PLAN
Objectives — The key functions planned for the complete embedded system
01 • DETECT
• Instant Sensing: Sense approaching emergency vehicles from North, East, South, and West using pushbuttons on GPIO External Interrupts (EXTI).
02 • TRANSITION
• Controlled Braking: Safely change conflicting green signals to yellow (2 s), followed by all-red (1 s), before granting emergency green.
03 • CLEAR
• Intersection Safety: Enforce a mandatory 1-second all-red clearance interval before and after every green phase so conflicting lanes never cross.
04 • ANTI-STARVATION
• Civilian Fairness: Limit consecutive ambulance runs to 2; then force a full normal green phase for whichever lane waited the longest.
05 • WARN & LOG
• Multi-Modal Alert: Drive an audible warning buzzer on PA7 during priority and stream real-time diagnostic state telemetry over USART2.
06 • QUEUE
• Zero Request Loss: Store concurrent or repeated emergency requests in memory and service them fairly in round-robin order.

## Slide 4
23CSE304 | EMBEDDED SYSTEMS 4 / 13
03 • SYSTEM DESIGN
System Block Diagram — Input stage → Controller & timing stage → Output stage
INPUTS INPUT & SENSING STAGE
• North Ambulance: Pushbutton on PA0 (Falling edge EXTI Line 0)
• East Ambulance: Pushbutton on PA1 (Falling edge EXTI Line 1)
• South Ambulance: Pushbutton on PA4 (Falling edge EXTI Line 4)
• West Ambulance: Pushbutton on PA8 (Falling edge EXTI Line 8)
• Internal Pull-Ups: Normally 3.3V (HIGH); pressing grounds the input to 0V (LOW).
• EXTI + NVIC: Asynchronous edge trigger immediately halts CPU wait-states.
PROCESSING EMBEDDED CONTROLLER
• Target MCU: STM32C031C6 (ARM Cortex-M0+ running at 12 MHz via HSI/4).
• Asynchronous ISR: Captures direction in < 2 µs and applies a 50 ms contact debounce filter.
• Non-Blocking FSM: State machine driven by HAL_GetTick() without frozen delays.
• Safety Interlock: Hardware SetAllRed() driver prevents overlapping greens.
• Fairness Engine: Enforces 2-ambulance maximum and tracks lane wait times.
OUTPUTS OUTPUT & ACTUATION STAGE
• Traffic LEDs (12 Pins): North: PB0/1/2 East: PB3/4/5 South: PB6/7/8 West: PB9/PC6/PC7
• Current Limiting: 220 Ω resistors ensure safe LED operating current.
• Audible Alert: Piezoelectric warning buzzer on PA7 sounds during emergency green & yellow.
• Telemetry Stream: USART2 TX on PA2 (115200 baud) prints real-time events.

## Slide 5
23CSE304 | EMBEDDED SYSTEMS 5 / 13
04 • IMPLEMENTATION
Hardware components, pin mapping, and software development toolchain
CIRCUIT LAYOUT HARDWARE COMPONENTS & PINOUT
• Controller: STM32C031C6 (ARM Cortex-M0+, 32 KB Flash, 12 KB SRAM).
• Traffic Signals: 12 active-high LEDs (Red, Yellow, Green for 4 approaches).
• Emergency Inputs: 4 pushbuttons with internal pull-ups on PA0, PA1, PA4, PA8.
• Warning Alert: Active buzzer driven by GPIO push-pull on PA7.
• Current Limiting: 220 Ω resistors on all 12 LED channels.
• Serial TX / RX: PA2 (USART2_TX) and PA3 (USART2_RX) at 115200 baud.
TOOLCHAIN SOFTWARE TOOLS & WORKFLOW
• STM32CubeMX: Visual chip configuration, pinout assignment, clock tree generation (HSI DIV4 = 12 MHz), and HAL startup code.
• STM32CubeIDE: Embedded C development, GNU ARM GCC toolchain, compilation, linker script mapping, and ELF binary generation.
• VS Code + Wokwi: Cycle-accurate virtual hardware simulation, interactive pushbutton clicks, LED rendering, and live Serial Monitor streaming.
• HAL & Non-Blocking: Uses STM32C0 HAL with HAL_GetTick() delta timing, eliminating processor-freezing HAL_Delay() loops.

## Slide 6
23CSE304 | EMBEDDED SYSTEMS 6 / 13
05 • CONTROL LOGIC
Controller State Machine — 6 Non-blocking phases governing the junction
REGULAR FLOW NORMAL TRAFFIC CYCLE
• Phase 1 • Normal Green (5 s): Active approach receives green; remaining 3 directions held red. Continuously scans for emergency requests.
• Phase 2 • Normal Yellow (2 s): Caution clearance phase; warns approaching cars to stop smoothly when time expires or an emergency occurs.
• Phase 3 • All-Red Clearance (1 s): All 4 approaches display red. Junction completely clears before switching to next direction.
• Autonomous Sequence: Rotates predictably: North → East → South → West → North.
EMERGENCY FLOW EMERGENCY PRIORITY PHASES
• Phase 4 • Ambulance Green (10 s): Requested approach gets green; buzzer turns ON at PA7; civilian traffic safely held red.
• Phase 5 • Ambulance Yellow (2 s): Caution transition as ambulance clears; buzzer remains ON to warn nearby drivers.
• Phase 6 • Ambulance All-Red (1 s): All red; buzzer turns OFF; scheduler checks whether another queued ambulance is waiting or if anti-starvation applies.
• Safety Guarantee: Direct green-to-green transitions are impossible — confirmed red required before any green turns on.

## Slide 7
23CSE304 | EMBEDDED SYSTEMS 7 / 13
06 • EMBEDDED ENGINEERING
Interrupt callback resolution, contact debouncing, and atomic bitmask latching
HAL INTEGRATION THE EXTI CALLBACK RESOLUTION
• The Challenge: In older STM32 families (F1/F4), a single HAL_GPIO_EXTI_Callback() handled all pin interrupts. In STM32C0, the HAL split this into separate Rising and Falling callbacks.
• The Discarded Symbol: Because our initial code implemented the legacy callback name, the STM32C0 linker discarded it as dead code, silently ignoring button presses.
• The Solution: Implementing HAL_GPIO_EXTI_Falling_Callback() properly overrode the weak HAL driver function, allowing button presses to trigger instantly.
• Microsecond Response: The ISR completes in < 2 µs by avoiding all blocking delays, logging, or LED operations inside interrupt context.
SIGNAL CONDITIONING DEBOUNCE & BITMASK QUEUEING
• Mechanical Chatter: Physical switches oscillate for milliseconds during closure, risking multiple false triggers per click.
• 50 ms Software Debounce: Independent lastPressTime[4] timestamp guard ensures that subsequent transitions within 50 ms are safely suppressed.
• Non-Destructive Bitmask: Valid requests set bits in pendingRequests |= (1U << dir). Duplicate clicks on the same button do not inflate the queue.
• Safe Acceptance: A request bit is cleared only when the controller officially accepts that ambulance into service.

## Slide 8
23CSE304 | EMBEDDED SYSTEMS 8 / 13
07 • FAIRNESS & ANTI-STARVATION
Preventing civilian traffic starvation during heavy consecutive emergency calls
URBAN TRAFFIC DILEMMA THE STARVATION THREAT
• Hospital Corridor Bottleneck: Intersections adjacent to medical centers frequently experience multiple emergency vehicles arriving in close succession.
• Civilian Gridlock: Naive priority systems keep extending emergency green, trapping civilian lanes at red for 5-10 minutes.
• Secondary Hazards: Frustrated drivers run red lights; blocked intersections create secondary gridlock that traps future ambulances.
• System Requirement: An embedded system must be both responsive to emergencies and fundamentally fair to general traffic.
SCHEDULER ARCHITECTURE THE DYNAMIC FAIRNESS ENGINE
• Configurable Limit: MAX_CONSECUTIVE_AMBULANCES = 2. Tracks consecutive emergency runs without civilian traffic.
• Wait-Time Tracking: Array lastNormalGreenTime[4] records the timestamp of when each lane last enjoyed a normal green phase.
• Guaranteed Civilian Phase: When the 2nd ambulance finishes, the system forces a full 5-second normal green for the longest-waiting lane.
• Uninterruptible Window: This anti-starvation phase cannot be cut short by new emergency requests.
• Zero Request Loss: Waiting ambulance requests remain safely queued in memory and resume immediately after the civilian phase finishes.

## Slide 9
23CSE304 | EMBEDDED SYSTEMS 9 / 13
08 • METHODOLOGY
Operating sequence — Step-by-step lifecycle of the junction controller
STEPS 1 - 4 DETECTION & PREEMPTION SEQUENCE
• Step 1 • Normal Operation: Junction rotates N → E → S → W using 5 s green, 2 s yellow, and 1 s all-red phases.
• Step 2 • Request Ingest: Ambulance button pulls pin to GND; EXTI triggers; ISR checks 50 ms debounce and sets direction bitmask.
• Step 3 • Controlled Braking: Conflicting active green transitions to yellow (2 s) and all-red (1 s) so cars clear the intersection safely.
• Step 4 • Priority Phase: Requested direction receives 10 seconds of green; warning buzzer sounds continuously on PA7.
STEPS 5 - 8 CLEARANCE & FAIRNESS SEQUENCE
• Step 5 • Exit Caution: Ambulance approach transitions to yellow (2 s) and all-red (1 s); warning buzzer shuts off.
• Step 6 • Anti-Starvation Check: If 2 consecutive ambulances have been served, grant a guaranteed 5 s normal green to the longest-waiting lane.
• Step 7 • Queue Service: If fewer than 2 ambulances or after civilian phase, service next pending emergency in round-robin sequence.
• Step 8 • Return to Normal: When queue is empty, resume normal rotation from the next approach in sequence.

## Slide 10
23CSE304 | EMBEDDED SYSTEMS 10 / 13
09 • SIMULATION & VALIDATION
Observable testing scenarios and real-time UART telemetry in Wokwi
WOKWI TEST BENCH TEST SCENARIOS VALIDATED
• Test 1 • Normal Cycle: Verified hands-free rotation through North, East, South, and West with exact 5s / 2s / 1s timing.
• Test 2 • Emergency Preemption: Pressed 'E' during North green. North safely transitioned to yellow (2s), all-red (1s), and East green lit for 10s with buzzer ON.
• Test 3 • Concurrent Queueing: Pressed 'S' and 'W' in rapid succession. South served first; West served immediately after without losing requests.
• Test 4 • Anti-Starvation Test: Triggered 'N', 'E', 'S'. First two served, then system forced a normal green for civilian traffic, then served 'S'.
• Safety Check: Zero overlapping greens across all tests; buzzer synchronized perfectly with priority.
CONSOLE LOGS LIVE SERIAL TELEMETRY (USART2)
• System Boot: [BOOT] Smart Ambulance Traffic Control Initialized
• Normal Cycle: [STATE] Normal traffic: NORTH GREEN (5000 ms)
• Transition: [STATE] Transition: NORTH YELLOW -> ALL RED
• Emergency Detect: [EVENT] Ambulance request received: EAST
• Priority Grant: [STATE] Ambulance priority granted: EAST (Consecutive: 1/2)
• Anti-Starvation: [ALERT] Anti-starvation triggered! Max 2 consecutive ambulances reached.
• Guaranteed Phase: [STATE] Granting guaranteed normal green to longest-waiting: SOUTH
• Baud Rate: 115200 baud, 8N1 formatted output.

## Slide 11
23CSE304 | EMBEDDED SYSTEMS 11 / 13
10 • SDG ALIGNMENT
United Nations Sustainable Development Goals — Health & Urban Mobility
UN SDG 3 SDG 3: GOOD HEALTH & WELL-BEING
• Target 3.6: Halving global deaths and injuries from road traffic accidents.
• Target 3.d: Strengthening early warning, risk reduction, and rapid emergency response.
• Preserving the Golden Hour: Reducing intersection transit delays directly improves survival rates in cardiac arrests, acute trauma, and stroke emergencies.
• Safe Transport: Eliminates dangerous, unpredictable intersection crossings, protecting both patients and paramedics.
UN SDG 11 SDG 11: SUSTAINABLE CITIES & COMMUNITIES
• Target 11.2: Providing access to safe, affordable, accessible, and sustainable transport systems for all.
• Urban Congestion Relief: Anti-starvation logic ensures regular commuter lanes and public transit are never permanently paralyzed by emergency traffic.
• Safe & Resilient Infrastructure: Mandatory yellow and all-red clearance intervals eliminate dangerous intersection collision risks.
• Reduced Carbon Emissions: Minimizing deadlocked traffic reduces unnecessary vehicle idling and localized greenhouse gas emissions.

## Slide 12
23CSE304 | EMBEDDED SYSTEMS 12 / 13
11 • APPLICATIONS & FUTURE SCOPE
Real-world smart city deployment and hardware sensor expansion
DEPLOYMENT POTENTIAL APPLICATIONS
• Hospital Emergency Corridors: Dynamic signal management along primary arterial roads connecting suburban highways to major trauma hospitals.
• Intelligent Transportation Systems (ITS): Integration with centralized municipal traffic management centers for coordinated green-wave corridors.
• Multi-Agency Emergency Preemption: Easily expandable to fire rescue engines, disaster response vehicles, and police convoys with multi-tier priority levels.
UPGRADES FUTURE HARDWARE EXPANSIONS
• V2X Wireless Transponders: Replacing pushbuttons with DSRC / C-V2X (Vehicle-to-Infrastructure) radio beacons transmitting emergency authentication.
• GPS Geo-Fencing: Automatically preempting intersection signals when an approaching ambulance enters a 500-meter threshold.
• Acoustic Siren Sensors: Directional microphone arrays tuned to emergency siren frequencies (750 Hz - 1.5 kHz) for automated detection.

## Slide 13
23CSE304 | EMBEDDED SYSTEMS 13 / 13
12 • CLOSING
Project summary, key achievements, and technical references
FINAL SUMMARY SUMMARY OF ACHIEVEMENTS
• Complete Embedded Firmware: Designed and verified a non-blocking state machine controller on the STM32C031C6 ARM Cortex-M0+ MCU.
• EXTI Callback Fix: Diagnosed and resolved the HAL_GPIO_EXTI_Falling_Callback linkage nuance in STM32C0.
• Safety Interlock: Hardware SetAllRed() driver physically eliminates conflicting green signals.
• Anti-Starvation Engine: Guarantees fair civilian traffic movement even during continuous emergency calls.
• Virtual Prototyping: Fully verified across 4 test scenarios using Wokwi simulation with live UART telemetry.
CITATIONS TECHNICAL REFERENCES
• Ref 1: STMicroelectronics, STM32C031x4/x6/x8 Reference Manual (RM0490).
• Ref 2: STMicroelectronics, STM32C031C6 Datasheet & STM32CubeC0 HAL Driver Documentation.
• Ref 3: IEEE, 'GPS and ZigBee Based Traffic Signal Preemption for Emergency Vehicles', ICICT, 2016.
• Ref 4: United Nations, Sustainable Development Goal 3: Good Health and Well-Being.
• Ref 5: United Nations, Sustainable Development Goal 11: Sustainable Cities and Communities.